## Slide 1
Design of stimuli-responsive materials from a diblock copolymer
with association between dissimilar monomers
MINGGE ZHAO, XINYUE ZHANG, JUNHAN CHO*
*DEPARTMENT OF POLYMER SCIENCE AND ENGINEERING, DANKOOK UNIVERSITY
*CORRESPONDENCE:JHCHO@DANKOOK.AC.KR
Abstract
Recently, stimuli-responsive materials have drawn tremendous attention due to their structures and properties and also due to their smart responses to changes in surrounding environment. In this work, we suggest the design of such materials based on associating A-b-B diblock copolymers. The free energy for the copolymer in the bulk state is first obtained as the perturbed hard sphere chains subject to adhesive potential between dissimilar monomers. Through Gaussian thread approach, the free energy functional is formulated to include effective local interactions from the excess equation of state. The random-phase approximation and self-consistent field analyses are to be readily elicited from the functional. It is demonstrated using these field approaches that the manipulation of disparity in self contact interactions and thermoreversibility of association can yield a variety of nasoscale mesophases upon cooling, heating, pressurization, and depressurization. In addition, micellization and reverse micellization in the solutions of the copolymer in selective solvents are to be probed via the manipulation of cross contact interactions and association. We will also discuss the applicability of such smart materials to various areas.
Introduction
Conclusion
Results and Discussion
Using random phase approximation and self-consistent field theory, the phase behaviors of associating diblock copolymer melts have been studied.
The thermal reversibility of polar bonds between dissimilar blocks affects the phase behavior of stimuli-responsive polymer systems.
Manipulating interactions and thermoreversibility yields various mesophases and the potential applications of smart materials are discussed.
Acknowledgment：National Research Foundation of Korea (Basic Science Research Program)
                                  
Background
◈ Random-phase approximation and Self-consistent field theory
Unconnected polar interactions
◈ Stimuli-responsive polymers
Spinodals from RPA and density profiles from SCFT
Dependence of UODT and LDOT on pressure
Free energy
Theory
Polystyrene-b-poly(n-pentyl methacrylate)
Poly(styrene)-b-poly(n-butyl methacrylate)
◈ Origin of LDOT of associating
A-b-B diblock copolymers system
Originated from polar bonds such as H-bonds
10
6
7
9
8
1
5
4
2
3
Polar interaction between i and j spheres
whose association is signified by
Associating A-b-B diblock copolymer melts
Reduction in Pressure due to polar bonding is described by the contact probability
The effective RPA interaction field is
given by the excess chemical potential
Hard sphere chain
Polar bonding
Dispersion energy
Du Ryu, Yeol, et al. "Closed-loop phase behaviour in block copolymers." Nature materials 1.2 (2002): 114-117.
Loop-forming A-b-B at ξ = 0.996515
T=480K
ΦA=0.49
(started from LAM)
xL=yL=~9.7
Loop-forming A-b-B at ξ = 0.99632
T=480K
ΦA=0.45
xL=yL=~3.8
Ps-b-P(n-butyl MA)
NA=557.2455, NB=557.6841
aτ=0.01468, ξAP=0.9879
T=500K
xL=yL=~3.8
T=400K
xL=yL=~3.8
Disorder
Since the density has hardly changed, it is disorder.
As the ξ approaches 1, the phase separation tendency is reduced and the loop becomes smaller.
The copolymer is ordered inside the loop and disordered outside the loop.
Ryu, Du Yeol, et al. "Effect of hydrostatic pressure on closed-loop phase behavior of block copolymers." Physical review letters 90.23 (2003): 235501.
Experimental:
Ps-b-P(n-butyl MA)
Ps-b-P(n-pentyl MA)
T sensitivity